## Slide 1: Design of FMCW Radar Based on Software Defined Radio with GNURadio for Detection, Range Estimation, and Velocity of an Object
Bima Pancara Haryono Putra
1101210528

## Slide 2: Outline
  Introduction
  Literature Review
  System Model and Design

## Slide 3
Sensing The World Through Sensor Technology

## Slide 5: Primary Goals
To Design FMCW Radar system based on USRP B210 with GNURadio.
To assess the detection, range estimation, and velocity of an object from the designed system.
To know the accuracy of detection, range estimation, and velocity of an object from the designed system.

## Slide 6
RAdio Detection And Ranging
Chain Home at RAF Poling, West Sussex

## Slide 15
Radar Cross Section

## Slide 16
Software Defined Radio

## Slide 17
Universal Software Radio Peripheral

## Slide 18
No. | Description | Value | Unit
1 | RF Coverage | 70 – 6 | MHz – GHz
2 | Analog to Digital Converter Sample Rate | 61,44 | MS/s
3 | Analog to Digital Resolution | 12 | bits
4 | Analog to Digital Wideband SFDR | 78 | dBc
5 | Digital to Analog Converter Sample Rate | 61,44 | MS/s
6 | Digital to Analog Resolution | 12 | bits
7 | Host Sample Rate (16b) | 61,44 | MS/s
8 | Frequency Accuracy | ± 2,0 | ppm
9 | W/ GPS Unlocked TCXO Reference | ± 75 | ppb
10 | W/ GPS Locked TCXO Reference | < 1 | ppb

## Slide 21
Research Parameter
Trial Parameter
Center Frequency | GHz
Bandwidth | MHz
Range | m
Velocity | m/s
RMSE | -

## Slide 22
No. | Spesification | Description
1 | USRP | B210
2 | Center Frequency | 3 GHz
3 | Bandwidth | 50 MHz
4 | Modulation | Triangular
5 | Maximum Range | 150 m
6 | Range Resolution | 3 m
7 | Maximum Velocity | 15 m/s
8 | Velocity Resolution | 1 m/s
9 | Chirp Time | 0,001667 s
10 | Chirp Rate | 30000 MHz

## Slide 23
Experiment Site

## Slide 24
Experiment Scheme

## Slide 25
Experiment Configuration

## Slide 26
Contribution
Test the accuracy of FMCW Radar design with GNURadio and implemented in B210 USRP to detect, range estimation, and velocity of an objet
As a reference on the implementation of FMCW Radar in many industry